## Slide 1: CFD pool fire simulations
UCT PRAGUE
Faculty of Chemical Engineering
Aleš Palkovič
Notes: Dear all, my name is Aleš. I am in 2nd year of my PHD studies and I am focused on CFD simulations. In my master thesis I have looked into a simulation of water mist suppression in Fluent. A lot of questions about turbulence and chemistry models.

## Slide 2: How to properly set up a simulation of a non-premixed combustion in Fluent?
Notes: Dear all, my name is Aleš. I am in 2nd year of my PHD studies and I am focused on CFD simulations. In my master thesis I have looked into a simulation of water mist suppression in Fluent. A lot of questions about turbulence and chemistry models.

## Slide 3: MaCFP
Systematic development of fire modelling
Database of experimental data
Compare simulation approaches
Generic SW - Ansys Fluent
  FDS
  OpenFOAM/FireFOAM
  In-house codes
Measurement and Computation of Fire Phenomena
International Association for Fire Safety Science

## Slide 4
Freestanding burner
Defined fuel flow rate
measurement
Experiment – methane burner
Falkenstein-Smith, R., K. Sung, J. Chen, and A. Hamins, Chemical Structure of Medium-Scale Liquid Pool Fires, Fire Safety Journal
D = 37 cm → D = 5 cm

## Slide 5: Ansys Fluent
Comertial, widely used in industry
Robust
Turbulence
Reaction

## Slide 6
Turbulence + mesh
Eddies
  Transport of energy
  Mixing
Smallest eddies: 4 cells
Fluctuation in time
Energy cascade →
Enegy dissipated into heat
Kolmogorov microscale

## Slide 7
Turbulence
Direct Numerical Simualtion (DNS)
Large Eddy Simulation (LES)
Reynolds Averaged Navier-Stokes (RANS)
Som, S., P. Senecal and E. Pomraning. “Comparison of RANS and LES Turbulence Models against Constant Volume Diesel Experiments.” (2012).
Notes: Pope – 80% kin. energie

## Slide 8
Methane burner – d = 50 mm
 | Estimate | RANS
Integral length scale (L) | 25 mm | 35 mm
Kolmogorov microslale (η) | 0.6 mm | 0.3 mm
Notes: Kolmogorov

## Slide 9
Appropriate cell size?
Recommendations:
  L/10 ≈ 2,5 mm (= D/20)
  D*/16 ≈ 3,2 mm (fine mesh - FDS)
Mesh sensitivity analysis
  Different mesh sizes
  Monitoring important quantities
Characteristic fire diameter
Notes: D*/4 coarse D*/10 medium

## Slide 10
Sensitivity analysis - RANS
Monitoring of HRR, steady state
3 types of meshes (6 mm)
6 mm 4 mm
3 mm
2 mm
1.5 mm
1 mm
Poly-hexcore
22 000
Hexcore
52 000
Polyhedra
12 000
2.2 mil
Notes: Rychlost vývinu tepla

## Slide 11
Sensitivity analysis - result
3 mm - suitable
Hexcore – diverged
Level of refinement | Cell size (mm)
1 | 6
2 | 4
3 | 3
4 | 2
5 | 1.5
6 | 1
Level of refinement

## Slide 12
LES
Cell size – 3 mm (89 000 cells)
Transient
Time step – 0.0001 s
  Data averaging (10 - 17 s)

## Slide 13
LES – 3 mm, results
Coarse mesh for LES?
RANS overpredicts?
Different temperature profile
Average HRR: 623 W
Same as in RANS

## Slide 14
LES – 2 mm, in progress
Cell size – 2 mm (295 000 cells)
Time step – 0.00005 s
Time consuming
Same results as LES 3mm?
  RANS overpredicts temperature
  LES in Fluent needs more refined mesh

## Slide 15
Conclusion and Next steps
Different results from RANS and LES with same mesh
Mesh sensitivity – universal tool for adequate mesh
Scale up to experiment dimensions
  Advances meshing methods

## Slide 16
Advanced methods
Body of Influence
Mesh adaptation

## Slide 17
CFD results are as precise…
… as the mesh defined by user.

## Slide 18
Thanks