## Slide 1: Inert Wall Exposed to Fire – Experiment and FDS Model
Supported by the Ministry of Interior, Safety research programme of the Czech Republic 2015–2022 (BV III/I - VS) under number VI20192022120 – Fire development modelling of engineered wood and by Specific university research grant No A1_FCHI_2022_005.
UNIVERSITY OF CHEMISTRY AND TECHNOLOGY
Department of Chemical Engineering
Laboratory of Fire Engineering
Vojtěch Šálek, Lucie Hasalová, Petr Hejtmánek

## Slide 2: Motivation – fire spread modeling
Engineered Wood Products (OSB, MDF, plywood,..)
CFD coupled to pyrolysis model
Complex modeling parameters
Pyr. gas composition
Soot yield
Density
Heat conductivity
Specific heat
Emissivity
Char density
Char heat cond.
Char specific heat
Char emissivity
Preexp. factor
Activation energy
Order of reaction
Heat of reaction
Heat of combustion
Stoch. coeff. of char
Stoch. coeff. of decomposing comp.

## Slide 3: Pyrolysis model input parameters
Micro-scale (TGA, DSC)
Bench-scale (Cone, Hot Disk)

## Slide 4: Validation of pyrolysis model
Vertical flame spread experiment
  Dataset covering flame spread
  2 x 1 m board
  50 x 5 x 10 cm propane burner
Combustible wall fire model
  Turbulent buoyant fluid model
  Gas phase kinetics
  Flame heat transfer
  Pyrolysis
Discrepancy related to pyrolysis only?
Wong, William Chiu-Kit. 2012. CFD Flame Spread Model Validation: Multi-Component Data Set Framework. : Worcester Polytechnic Institute

## Slide 5: Inert wall fire
Thermal feedback to the wall
Fiber cement panel
  2 x 1 m
  12 mm thick
  Back side exposed

## Slide 6: Inert wall measured quantities
Gas phase
  Temperature in the corner
  Temperature close to the panel
  Net heat flux to the wall
Solid phase
  Surface temperature front and back

## Slide 7: Repeatability and uncertainty
5 times at each heat flux (30 and 50 kW)
Max-min values showed for 30 kW
  25 °C ± 2.5 °C
  90 °C ± 3.8 °C
Net heat flux
    Calibration accuracy is ± 3 % at full scale
    Non-linearity error 10 - 50 %

## Slide 8: Model
FDS (Fire Dynamic Simulator) ver. 6.7.7
Layout (ISO 9705-1) modified according to experiments

## Slide 9: Model – boundary conditions
&SURF ID=‚FLOOR',
BACKING='VOID',
MATL_ID(1,1)=' AERATED_CONCRETE ',
MATL_MASS_FRACTION(1,1)=1.0,
THICKNESS(1)=0.1,/
&SURF ID='VENTILATOR',
VOLUME_FLOW=0.8 / (m3/s)
&VENT SURF_ID='OPEN'/
&MATL ID=‚AERATED_CONCRETE',
SPECIFIC_HEAT=1.0,
CONDUCTIVITY=0.12,
DENSITY=500.0/
&OBST SURF_ID='INERT', TRANSPARENCY=0.5 /

## Slide 10: Model – boundary conditions
&SURF ID=‚CEILING',
COLOR='BLACK',
BACKING='VOID',
MATL_ID(1,1)='FERMACELL_AESTUVER',
MATL_ID(2,1)='MINERAL_WOOL',
MATL_ID(3,1)='YTONG',
THICKNESS(1)=0.020,
THICKNESS(2)=0.030,
THICKNESS(3)=0.2, /
&MATL ID='FERMACELL_AESTUVER',
SPECIFIC_HEAT=0.9,
CONDUCTIVITY=0.21,
DENSITY=800.0 /
&MATL ID='MINERAL_WOOL',
SPECIFIC_HEAT=0.94,
CONDUCTIVITY=0.035,
DENSITY=35.0 /
&MATL ID='YTONG',
SPECIFIC_HEAT=1.0,
CONDUCTIVITY=0.10,
DENSITY=400.0/

## Slide 11: Model – boundary conditions
&SURF ID='BURNER',
COLOR='RED'
HRRPUA=1200.0 /
Burner (30 kW)
50 x 5 x 10 cm
&SURF ID='INERT_WALL',
COLOR='WHITE',
BACKING='EXPOSED',
MATL_ID(1,1)= 'FERMACELL_POWERPANEL',
MATL_MASS_FRACTION(1,1)=1.0,
STRETCH_FACTOR(1)=1,
CELL_SIZE_FACTOR=0.5,
THICKNESS(1)=0.0125 /
&MATL ID= 'FERMACELL_POWERPANEL',
SPECIFIC_HEAT=1.0,
CONDUCTIVITY=0.17,
DENSITY=1000.0 /
Inert wall 2 x 1 x 0,0125 m

## Slide 12: Model – inert wall
&SURF ID='INERT_WALL',
COLOR='WHITE',
BACKING='EXPOSED',
MATL_ID(1,1)= 'FERMACELL_POWERPANEL',
MATL_MASS_FRACTION(1,1)=1.0,
STRETCH_FACTOR(1)=1,
CELL_SIZE_FACTOR=0.5,
THICKNESS(1)=0.0125 /
BACKING='EXPOSED'
  Influences heat conduction
  Maximum one cell thick objects

## Slide 13: Model – inert wall
BACKING='EXPOSED'
  Influences heat conduction
  Maximum one cell thick objects
&SURF ID='INERT_WALL',
COLOR='WHITE',
BACKING='EXPOSED',
MATL_ID(1,1)= 'FERMACELL_POWERPANEL',
MATL_MASS_FRACTION(1,1)=1.0,
STRETCH_FACTOR(1)=1,
CELL_SIZE_FACTOR=0.5,
THICKNESS(1)=0.0125 /

## Slide 14: Model – inert wall
BACKING='EXPOSED'
  Influences heat conduction
  Maximum one cell thick objects
&SURF ID='INERT_WALL',
COLOR='WHITE',
BACKING='EXPOSED',
MATL_ID(1,1)= 'FERMACELL_POWERPANEL',
MATL_MASS_FRACTION(1,1)=1.0,
STRETCH_FACTOR(1)=1,
CELL_SIZE_FACTOR=0.5,
THICKNESS(1)=0.0125 /

## Slide 15: Model – inert wall
&SURF ID='INERT_WALL',
COLOR='WHITE',
BACKING='EXPOSED',
MATL_ID(1,1)= 'FERMACELL_POWERPANEL',
MATL_MASS_FRACTION(1,1)=1.0,
STRETCH_FACTOR(1)=1,
CELL_SIZE_FACTOR=0.5,
THICKNESS(1)=0.0125 /
First cell size calculated as
Number and size of additional cells
  Default:
    stretch factor = 2 (x times previous cell)
    cell size factor = 1 (x times first cell)

## Slide 16: Model – combustion
Reaction in gas phase
  ideal combustion of propane
&REAC ID='PROPANE',
FUEL='PROPANE',
SOOT_YIELD=0.0
CO_YIELD=0.0 /
  No soot formation assumed

## Slide 17: Model – computational mesh
Computational mesh analysis is basic assumption for good model prediction
Cell size necessary to solve boundary layer and temperature gradient in the wall is in order of 1 mm [1]
  Extreme computational demands
  FDS restricted to structured meshes
  ~ 800 000 cells/mesh
[1] Brown, A., Bruns, M., Gollner, M., Hewson, J., Maragkos, G., Marshall, A., McDermott, R., Merci, B., Rogaume, T., Stoliarov, S., Torero, J., Trouvé, A., Wang, Y., Weckman, E. (2018). Proceedings of the First Workshop Organized by the IAFSS Working Group on Measurement and Computation of Fire Phenomena (MaCFP), Fire Safety Journal, 101, 1-17.

## Slide 18: Model – computational mesh
Model label | Cell size in direction perpendicular to the panel | Total number of cells | Number of meshes | Simulation time (s)
1 mm | 1 mm – 2 mm - 4 mm – 2 cm | 65 902 500 | 80 | 10 s
2 mm | 2 mm - 4 mm - 8 mm – 4 cm | 22 222 800 | 36 | 40 s
2 cm | 1 cm – 2 cm - 10 cm | 804 084 | 11 | 600 s
5 cm | 1 cm - 5 cm | 1 070 496 | 6 | 600 s
10 cm | 1 cm - 10 cm | 637 812 | 6 | 600 s
Restrictions in burner size, distance from burner to wall and conditions of „backing“
Large jumps between individual
Near wall vs. far from wall

## Slide 19: Results – cold layer 670 mm

## Slide 20: Results – cold layer 970 mm
  Δ 5 °C 15 %
Both height 670 and 970 mm safely in cold layer
Independent of mesh density

## Slide 21: Results – hot layer 1720 mm
  Δ 10 °C 12.5 %

## Slide 22: Results – heat flux to the wall
Significantly higher scatter of values for milimeter size meshes

## Slide 23: Results – heat flux to the wall
Symetrical model behaviour compared to experiment
Net heat flux measured, radiometer is cooled compared to wall

## Slide 24: Results – center surface temperature
Mesh density has no influence
Moisture
Constant k and cp

## Slide 25
Moisture, constant k and cp
Mesh density has an influence
1D heat transfer
Results – center surface temperature

## Slide 26
Results – center surface temperature
Moisture, constant k and cp
Mesh density has an influence
1D heat transfer

## Slide 27: Conclusions
A lot of work to do in the future
Experiments
  Use heat flux gauges with lower measuring range
  Measure velocity profile in the doors
Model
  Need of milimeter-size mesh confirmed
  Change the boundary condition in the hood area
  Add temperature dependent parameters
  The effect of 3D conduction
  Get at least 200 seconds of the very fine meshes

## Slide 28
Thank you for you attention!